The following ports need to be opened at least to the target address in order to allow H.323 (IP) Video Conferencing packets- Both incoming and outgoing:

- 80 - Static TCP - HTTP Interface (optional

- 389 - Static TCP - ILS Registration (LDAP)

- 1503 - Static TCP - T.120

- 1718 - Static UDP - Gatekeeper discovery (Must be bidirectional

- 1719 - Static UDP - Gatekeeper RAS (Must be bidirectional)

- 1720 - Static TCP - H.323 call setup (Must be bidirectional)

- 1731 - Static TCP - Audio Call Control (Must be bidirectional)

- 8080 - Static TCP - HTTP Server Push (optional)

For RTP Traffic

- 1024-65535 Dynamic TCP H245

- 1024-65535 Dynamic UDP - RTP (Video data)

- 1024-65535 Dynamic UDP - RTP (Audio data)

- 1024-65535 Dynamic UDP RTCP (Control Information)

The above configuration will allow making point-to-point call between any two sites.